## Slide 1
IMAGE PROCESSING · MINI PROJECT
Concrete Crack Detection
Automated detection of structural cracks on concrete surfaces using traditional image-processing techniques
Presented by Member 1 · Member 2 · Member 3
Notes: [Member 1] Hi everyone. Today our group presents our project, Concrete Crack Detection.

## Slide 2
Problem & Motivation
Why automatic crack detection matters
Last year's earthquake affecting Thailand raised strong awareness about the safety of buildings and infrastructure. Cracks on concrete walls and columns are one of the earliest warning signs of structural deterioration — but manual visual inspection over large or hard-to-reach areas is slow and error-prone.
1
First warning sign Cracks signal early structural deterioration
2
Hard to access Large areas & tight spots are unsafe to inspect by hand
3
Slow & error-prone Human visual inspection wastes time and misses defects
Notes: [Member 1] The idea started with last year's earthquake affecting Thailand, which put building safety in the spotlight. Cracks on concrete walls and columns are one of the earliest warning signs of deterioration, but inspecting large or hard-to-reach areas by eye is slow and easy to get wrong.

## Slide 3
Objective & Scope
Objective Build an image-processing system that automatically detects and outlines cracks on concrete — and separates real structural cracks from normal rough texture or stains.
Goal
A prototype that takes a concrete photo and highlights crack regions as a mask
Technique
Traditional image processing first — no large deep-learning model, to prove the math
Dataset
Public sets with pixel-level ground-truth masks: CrackForest, Crack500, DeepCrack
Team scale
Designed for a 2–3 person team: image prep, algorithm tuning, evaluation
Notes: [Member 1] Our goal is a program that detects cracks automatically and tells real cracks apart from normal rough texture or stains. We deliberately use traditional image processing first, no large deep-learning model, to prove the underlying math. We test on public datasets with pixel-level ground-truth masks such as CrackForest and Crack500. Next, [Member 2] will walk through how it works.

## Slide 4
Method — 4-Step Pipeline
From raw photo to a clean crack mask
1
Pre-processing
Grayscale, Gaussian blur to cut noise, CLAHE contrast so dark cracks stand out
2
Segmentation
Adaptive Thresholding (vs. Otsu) isolates dark pixels into a binary mask
3
Morphological Filtering
Closing reconnects broken cracks; Opening removes small noise blobs
4
Shape Analysis
Filter contours by area & aspect ratio — real cracks are thin & long
Output: a binary mask that highlights only genuine cracks.
Notes: [Member 2] Our method has four main steps. First, pre-processing: convert to grayscale, reduce noise with Gaussian blur, and boost contrast with CLAHE so dark cracks stand out. Second, segmentation: Adaptive Thresholding pulls out the darker pixels into a binary mask — we chose adaptive because it handles uneven lighting better than global Otsu. Third, morphological filtering: Closing reconnects broken cracks and Opening removes small noise. Finally, shape analysis: we filter contours by area and aspect ratio, since real cracks are thin and long, unlike round pores or stains. Now [Member 3] will cover results and where this goes next.

## Slide 5
Expected Results & Evaluation
Expected Output
Binary mask highlighting only crack lines
Filters out noise from rough texture, pores, and shadows
Works under moderately controlled lighting
Pixel-Level Metrics
Compare the predicted mask against the ground-truth mask, pixel by pixel.
Precision Correctly predicted crack pixels — cuts false alarms
Recall Real crack pixels found — cuts missed cracks
IoU & Dice / F1 Mask overlap — the standard for imbalanced segmentation
Notes: [Member 3] We expect the program to produce a binary mask that highlights only crack lines and filters out noise from texture, pores, and shadows. For evaluation we work at the pixel level, comparing our mask to the ground-truth mask, and compute Precision, Recall, and especially IoU and Dice score — the standard metrics for segmentation, which suit crack data where crack pixels are heavily imbalanced, better than accuracy alone.

## Slide 6
Future Work
Toward Edge AI & drone-based inspection
1
Optimize
Make the algorithm lightweight enough to run on small boards
2
Embed
Deploy on ESP32, STM32 or FPGA hardware
3
Fly
Mount on inspection drones for façades and under-bridge gaps
4
Alert
Send crack alerts with location back to a central system
Thank you
Questions welcome
Notes: [Member 3] Finally, this can go much further. We plan to optimize the algorithm to run on small boards like ESP32 or FPGA, mount it on inspection drones to reach façades and under-bridge gaps, and send crack alerts with coordinates to a central system in real time. That's our project — thank you.